## Slide 1: 2010 “Outside ROW Working group”
What was outdated in MAG
Peter Kandaris

## Slide 2
REVIEW OF MAG UNIFORM STANDARD SPECIFICATIONS FOR PUBLIC WORKS CONSTRUCTION |  | 
Outside Right-of-Way Working Group - Sections |  | 
Section | Title | Recommended Action
225 | Watering | Delete this section since it provides minimal technical guidance - mostly general conditions. Modify earthwork and dust control specifications if needed and include general conditions in Section 104.
301 | Subgrade Preparation | Include a section on geotechnical investigation information; check ASTM references; delete reference to Detail 190 and reference ASTM D4718; clarify subgrade stability below pavements.
309 | Lime Slurry Stabilization | Re-write this section to be current with modern methods
310 | Untreated Base | Change the title to provide clarity; modify Table 310-1 to make correction of deficiencies applicable to present needs and methods.
311 | Soil Cement Base Course | Change the title to indicate cement stabilization of native soil (not ABC); spec needs review and revision to make current with modern methods
313 | Bituminous Treated Base Course | Remove from MAG as this proceedure is no longer used.
323 | Heater Remix Resurfacing | Remove from MAG ; this section probably does not meet ADEQ air quality regulations.
334 | Preservative Seal for Asphalt Concrete | Revise specification for modern seal coats presently used and delete reference to rejuvanating agents that probably do not meet ADEQ air quality regulations.
335 | Hot Asphalt-rubber Seal | Either delete or make current with modern methods.
337 | Pavement Crack Repair | Suggested new MAG specification to meet current agency practices
342 | Decorative Pavement Concrete Paving Stone or Brick | Remove material references from this placement specification and place them in their appropriate locations in Part 700.
350 | Removal of Exisitng Improvements | Modify to include utility abandonment/removal requirements.
360 | Telecommunications Installations | Revise to meet current agency practices and requirements.
401 | Traffic Control | Revise to meet current agency practices and requirements.
410 | Precast Safety Curbs | Remove from MAG as this is for outside of ROW locations.
430 | Landscaping and Planting | Revise to include current practices and innovations (hydroseeding)
440 | Sprinkler Irrigation System Installation | Revise to include current practices and innovations (drip systems)
501 | Driving Piles | Delete this section as it is outdated, rarely used and partly a design document.
515 | Steel Structures | Revise section to delete references to major structures that fall under building code regulations; section should be for minor steel strucutures only.
520 | Steel and Aluminum Handrails | Revise to match existing details and current codes/standards.
525 | Pneumatically Placed Mortar | Revise to include current practices and correct ACI references/requirements.
530 | Painting | Section is outdated and needs to be revised to meet current industry standards.
601 | Trench Excavation, Backfilling And Compaction | Include a section on geotechnical investigation information.
605 | Subdrainage | Antiquated specification. Update for current practices and material placement methods.
621 | Corrugated Metal Pipe And Arches | Revise to remove out-of-date practices.
630 | Tapping Sleeves, Valves And Valve Boxes On Water Lines | Revise to remove specified products - make requirements generic.
640 | Precast Concrete Arches | Suggested new MAG specification to meet current agency practices
705 | Portland Cement Treated Base | Table 705-1 has an error in the specified -#200 range (blooper case).
709 | Recycled Asphalt Pavement | ARPA suggests minor changes to better meet current materials.
715 | Slurry Seal Materials | ARPA suggests minor changes to better meet current materials.
719 | Recycled Asphalt Concrete - Hot Mixed | ARPA suggests minor changes to better meet current materials.
729 | Expansion Joint Material | Materials and ASTM references may be out of date. To be reviewed by the Concrete Working Group.
736 | Non-reinforced Concrete Pipe | MAG committee should review to determine if this material is still desired.
751 | Gray Iron Pipe and Fittings | Suggested new MAG specification to meet current agency practices.
754 | Copper Pipe, Tubing and Fittings | Revise to include Type M copper.
757 | Sprinkler Irrigation Systems | Suggest changing title to "Landscape Irrigation" and update for current materials (drip systems).
770 | Structural And Rivet Steel, Rivets, Bolts, Pins, And Anchor Bolts | Antiquated specification. Update for current materials.
772 | Chain Link Fence | Review and change ASTM standards that are out of date.
776 | Masonry Mortar and Grout | Section is outdated and needs to be revised to meet current industry standards.
778 | Lumber | Section is outdated and needs to be revised to meet current industry standards.
779 | Wood Preservatives | Section is outdated and needs to be revised to meet current industry standards.
780 | Timber Piles | Delete this section as it is outdated, rarely used and provides little guidance.
781 | Steel Piles | Delete this section as it is outdated, rarely used and provides little guidance.
782 | Concrete Piles | Delete this section as it is outdated, rarely used and provides little guidance.
785 | Steel Castings | Remove from MAG as these materials are no longer used.
786 | Bronze Casting | Remove from MAG as these materials are no longer used.
787 | Gray Iron Castings | Delete this section; place essential information from 787.3 in existing details referencing gray iron castings.
790 | Paint | Section is outdated and needs to be revised to meet current industry standards.
795 | Landscaping Material | Revise to include current materials used by agencies.
Outside “Right of Way” working group list
Notes: REVIEW OF MAG UNIFORM STANDARD SPECIFICATIONS FOR PUBLIC WORKS CONSTRUCTION Outside Right-of-Way Working Group - Sections

## Slide 3
REVIEW OF MAG UNIFORM STANDARD DETAILS FOR PUBLIC WORKS CONSTRUCTION |  | 
Outside Right-of-Way Working Group - Details |  | 
Detail | Title | Recommended Action
131 | Street Sign Base | Update to include materials currently used by agencies for street sign supports.
135 | Steel Guard Rail | Include end attenuation details.
150 | Precast Safety Curb | Delete from ROW standard as these are used outside ROW.
160 | Chain Link Fence and Gate | Include options for higher fencing as allowed in Section 420.
170 | Typical Runway or Taxiway Edge Lighting Detail | Delete from ROW standard. Detail is for work outside of the ROW and may not be current.
190 | Rock Correction Procedure for Maximum Density Determination | Delete from ROW construction standard. This is a QC testing requirement that can be specified in Section 301 using ASTM D4718.
202 | Alley Details | Modify inverted crown alley for access road use; delete unpaved surface or include aggregate or RAP surfacing
204 | Equipment Crossing | Review to determine if this is still needed. When would it be used?
210 | Residential Speed Hump | Include option for speed table (Tempe design); include a note on drainage impacts.
225 | Concrete Pavers | Include colored pavers, textured concrete and formed pavers.
270 | Frame & Cover (and Grade Adjustments) | Delete "AND GRADE ADJUSTMENTS" from the Table of Contents title and from the detail subtitle. Prepare a new detail for grade adjustments for overlays.
301 | Blocking for Water Gate and Butterfly Valves | Review to determine if a detail is needed for butterfly valves.
302 | Joint Restraint with Tie Rods | Change detail to match current methods - use of megalugs or equal.
321 | Standard Water Meter Vault | Review to determine if the detail matches current practices.
340 | Installing Tapping Sleeves and Valves | Evaluate removing stainless steel option as they are difficult to get water tight.
346 | Fire Line Detector Check Valve | Review and determine if this detail belongs in a ROW specification (move to outside ROW standard?).
360 | Fire Hydrant Installation | Revise to include standard collar type, add below grade shear collar, include minimum height above grade.
370 | Vertical Realignment of Water Mains | Determine if case from a few years ago is still applicable.
380 | Thrust Blocks for Water Lines | Revise to show blocks to scale, inlcude options for soil capacities less than 3000 psi.
389 | Curb Stop with Valve Box and Cover | Revise to make consistent with current practices.
390 | Curb Stop with Flushing Pipes | Revise to make consistent with current practices.
392 | Debris Cap Installation | Review to determine if the detail is still used or necessary. This one can probably be deleted.
402 | Encased Pipe for Canal Crossing | Recommend deleting the detail since irrigation agency standards supercede MAG on canals.
405 | Broken Sewer Line Replacement | Detail appears to apply to only clay pipe. Expand to include more types of sewer pipe.
424 | 24" and 30" Manhole Frame and Cover | Revise tolerance to allow fabrication in the US.
425 | 24" Aluminum Manhole Frame and Cover | Recommend deleting the detail as it is rarely (if ever) used.
426 | Drop Sewer Connection | Detail needs clarification and to be expanded for more than just clay pipe.
427 | Stub Out and Plugs | Modify to include caps, blocking details and mechanical seal.
441 | Sewer Cleanout | Modify to include testing requirements and vertical pipe distance.
504 | Concrete Block Junction Box | Review to determine if covers are consistent with current practices.
505 | Concrete Pipe Collars | Detail needs to be cleaned up and be consistent with current practices.
507 | Encased Concrete Pipe (for Shallow Installation) | Method of pipe protection is vague and needs to be better engineered to determine if it really works. Is it really needed or wanted?
524 | Storm Drain Lateral Pipe Connections | Review to determine if this belongs in a ROW standard.
550 | Spillway Inlet and Outlet | Modify to include grouted riprap option.
729 | Expansion Joint Material | Materials and ASTM references may be out of date. To be reviewed by the Concrete Working Group.
345-1 | 3", 4" and 6" Water Meter | Review - may not be in accordance with current agency practices.
391-1&2 | Valve Box Installation and Grade Adjustment | Revise to include use outside pavements and out of ground. Incorporate numerous city supplement options.
420-1&2 | Precast Concrete Sewer Manhole | Revise to delete reference to propriatary products and include options for overexcavation and recompaction.
502-1&2 | Trash Rack | Revise to make consistent with current practices.

## Slide 4
Cases for Removal from MAG Specifications and Details (2011) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
313 | Bituminous Treated Base Course | Delete this section as this proceedure is no longer used.
410 | Precast Safety Curbs | Delete this section as this is for outside of ROW locations.
501 | Driving Piles | Delete this section as it is outdated, rarely used and partly a design document.
780 | Timber Piles | Delete this section as it is outdated, rarely used and provides little guidance.
781 | Steel Piles | Delete this section as it is outdated, rarely used and provides little guidance.
782 | Concrete Piles | Delete this section as it is outdated, rarely used and provides little guidance.
785 | Steel Castings | Delete this detail as these materials are no longer used.
786 | Bronze Casting | Delete this detail as these materials are no longer used.
Detail | Title | Recommended Action by Outside ROW Working Group
150 | Precast Safety Curb | Delete from ROW standard as these are used outside ROW.
170 | Typical Runway or Taxiway Edge Lighting Detail | Delete from ROW standard. Detail is for work outside of the ROW and may not be current.
402 | Encased Pipe for Canal Crossing | Delete this detail since irrigation agency standards supercede MAG on canals.
425 | 24" Aluminum Manhole Frame and Cover | Delete this detail as it is rarely (if ever) used.

## Slide 5
Cases for Removal from MAG Specifications and Details - Minor Changes Needed in Other Standards/Details (2011) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
225 | Watering | Delete this section since it provides minimal technical guidance - mostly general conditions. Modify earthwork and dust control specifications if needed and include general conditions in Section 104.
787 | Gray Iron Castings | Delete this section; place essential information from 787.3 in existing details referencing gray iron castings.
Detail | Title | Recommended Action by Outside ROW Working Group
190 | Rock Correction Procedure for Maximum Density Determination | Delete from ROW construction standard. This is a QC testing requirement that can be specified in Section 301 using ASTM D4718.

## Slide 6
Cases for Review by Concrete Working Group (2011)(green shading denotes minor revisions) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
342 | Decorative Pavement Concrete Paving Stone or Brick | Remove material references from this placement specification and place them in their appropriate locations in Part 700.
525 | Pneumatically Placed Mortar | Revise to include current practices and correct ACI references/requirements.
640 | Precast Concrete Arches | Suggested new MAG specification to meet current agency practices
776 | Masonry Mortar and Grout | Section is outdated and needs to be revised to meet current industry standards.
Detail | Title | Recommended Action by Outside ROW Working Group
225 | Concrete Pavers | Include colored pavers, textured concrete and formed pavers.
550 | Spillway Inlet and Outlet | Modify to include grouted riprap option.
729 | Expansion Joint Material | Materials and ASTM references may be out of date.

## Slide 7
Cases for Review by Asphalt Working Group (2011) (green shading denotes minor revisions) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
323 | Heater Remix Resurfacing | Revise to make current with new practices and in line with air regulations.
334 | Preservative Seal for Asphalt Concrete | Revise specification for modern seal coats presently used and delete reference to rejuvanating agents that probably do not meet ADEQ air quality regulations.
335 | Hot Asphalt-rubber Seal | Either delete or make current with modern methods.
337 | Pavement Crack Repair | Suggested new MAG specification to meet current agency practices
709 | Recycled Asphalt Pavement | Minor changes needed to better meet current materials.
715 | Slurry Seal Materials | Minor changes needed to better meet current materials.
719 | Recycled Asphalt Concrete - Hot Mixed | Minor changes needed to better meet current materials.

## Slide 8
Cases for Review by Sewer & Water Working Group (green shading denotes minor revisions) (2011) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
630 | Tapping Sleeves, Valves And Valve Boxes On Water Lines | Revise to remove specified products - make requirements generic.
640 | Precast Concrete Arches | Suggested new MAG specification to meet current agency practices
736 | Non-reinforced Concrete Pipe | Review to determine if this material is still desired.
751 | Gray Iron Pipe and Fittings | Suggested new MAG specification to meet current agency practices.
754 | Copper Pipe, Tubing and Fittings | Revise to include Type M copper.
Detail | Title | Recommended Action by Outside ROW Working Group
301 | Blocking for Water Gate and Butterfly Valves | Review to determine if a detail is needed for butterfly valves.
302 | Joint Restraint with Tie Rods | Change detail to match current methods - use of megalugs or equal.
321 | Standard Water Meter Vault | Review to determine if the detail matches current practices.
340 | Installing Tapping Sleeves and Valves | Evaluate removing stainless steel option as they are difficult to get water tight.
346 | Fire Line Detector Check Valve | Review and determine if this detail belongs in a ROW specification (move to outside ROW standard?).
360 | Fire Hydrant Installation | Revise to include standard collar type, add below grade shear collar, include minimum height above grade.
370 | Vertical Realignment of Water Mains | Determine if case from a few years ago is still applicable.
380 | Thrust Blocks for Water Lines | Revise to show blocks to scale, inlcude options for soil capacities less than 3000 psi.
389 | Curb Stop with Valve Box and Cover | Revise to make consistent with current practices.
390 | Curb Stop with Flushing Pipes | Revise to make consistent with current practices.
392 | Debris Cap Installation | Review to determine if the detail is still used or necessary. This one can probably be deleted.
405 | Broken Sewer Line Replacement | Detail appears to apply to only clay pipe. Expand to include more types of sewer pipe.
424 | 24" and 30" Manhole Frame and Cover | Revise tolerance to allow fabrication in the US.
426 | Drop Sewer Connection | Detail needs clarification and to be expanded for more than just clay pipe.
427 | Stub Out and Plugs | Modify to include caps, blocking details and mechanical seal.
441 | Sewer Cleanout | Modify to include testing requirements and vertical pipe distance.
504 | Concrete Block Junction Box | Review to determine if covers are consistent with current practices.
505 | Concrete Pipe Collars | Detail needs to be cleaned up and be consistent with current practices.
507 | Encased Concrete Pipe (for Shallow Installation) | Method of pipe protection is vague and needs to be better engineered to determine if it really works. Is it really needed or wanted?
524 | Storm Drain Lateral Pipe Connections | Review to determine if this belongs in a ROW standard.
345-1 | 3", 4" and 6" Water Meter | Review - may not be in accordance with current agency practices.
391-1&2 | Valve Box Installation and Grade Adjustment | Revise to include use outside pavements and out of ground. Incorporate numerous city supplement options.
420-1&2 | Precast Concrete Sewer Manhole | Revise to delete reference to propriatary products and include options for overexcavation and recompaction.
502-1&2 | Trash Rack | Revise to make consistent with current practices.

## Slide 9
Cases for Review by Materials Working Group (new) (green shading denotes minor revisions) (2011) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
301 | Subgrade Preparation | Include a section on geotechnical investigation information; check ASTM references; delete reference to Detail 190 and reference ASTM D4718; clarify subgrade stability below pavements.
309 | Lime Slurry Stabilization | Re-write this section to be current with modern methods
310 | Untreated Base | Change the title to provide clarity; modify Table 310-1 to make correction of deficiencies applicable to present needs and methods.
311 | Soil Cement Base Course | Change the title to indicate cement stabilization of native soil (not ABC); spec needs review and revision to make current with modern methods
601 | Trench Excavation, Backfilling And Compaction | Include a section on geotechnical investigation information.
605 | Subdrainage | Antiquated specification. Update for current practices and material placement methods.
621 | Corrugated Metal Pipe And Arches | Revise to remove out-of-date practices.
Detail | Title | Recommended Action by Outside ROW Working Group
270 | Frame & Cover (and Grade Adjustments) | Delete "AND GRADE ADJUSTMENTS" from the Table of Contents title and from the detail subtitle. Prepare a new detail for grade adjustments for overlays.

## Slide 10
Cases for Review by Various Members & Agency Staff (green shading denotes minor revisions)(2011) |  | 
Section | Title | Recommended Action by Outside ROW Working Group
350 | Removal of Exisitng Improvements | Modify to include utility abandonment/removal requirements.
360 | Telecommunications Installations | Revise to meet current agency practices and requirements.
401 | Traffic Control | Revise to meet current agency practices and requirements.
430 | Landscaping and Planting | Revise to include current practices and innovations (hydroseeding)
440 | Sprinkler Irrigation System Installation | Revise to include current practices and innovations (drip systems)
515 | Steel Structures | Revise section to delete references to major structures that fall under building code regulations; section should be for minor steel strucutures only.
520 | Steel and Aluminum Handrails | Revise to match existing details and current codes/standards.
530 | Painting | Section is outdated and needs to be revised to meet current industry standards.
757 | Sprinkler Irrigation Systems | Suggest changing title to "Landscape Irrigation" and update for current materials (drip systems).
770 | Structural And Rivet Steel, Rivets, Bolts, Pins, And Anchor Bolts | Antiquated specification. Update for current materials.
772 | Chain Link Fence | Review and change ASTM standards that are out of date.
779 | Wood Preservatives | Section is outdated and needs to be revised to meet current industry standards.
790 | Paint | Section is outdated and needs to be revised to meet current industry standards.
795 | Landscaping Material | Revise to include current materials used by agencies.
Detail | Title | Recommended Action by Outside ROW Working Group
131 | Street Sign Base | Update to include materials currently used by agencies for street sign supports.
135 | Steel Guard Rail | Include end attenuation details.
160 | Chain Link Fence and Gate | Include options for higher fencing as allowed in Section 420.
202 | Alley Details | Modify inverted crown alley for access road use; delete unpaved surface or include aggregate or RAP surfacing
204 | Equipment Crossing | Review to determine if this is still needed. When would it be used?

## Slide 11: Activity Prior to 2010
2005: 5 considered, 5 approved
2006: 9 considered, 8 approved
2007: 15 considered, 9 approved
2008: 22 considered, 15 approved
2009: 16 considered, 13 approved
2010: 16 considered, 12 approved
2011: 37 considered, 27 approved
2012: 20 considered, 17 approved

## Slide 12: Asphalt Working Group
2011 major case revisions:
327 Hot in-place recycling
711 paving asphalt binder specifications
332,715 slurry seal
334,718 preservative seal
325, 717 Asphalt Rubber
335 Asphalt Rubber chip
321 placement of asphalt pavement
337 crack sealing

## Slide 13: 321 changes
Owner/Agency distinction
Compaction issues addressed
Self directed target changes for producers
Void and binder content requirements
Sample frequency depending on project size

## Slide 14: 337 Crack sealing specification
Brand new section
Most popular products included
Application very easy to understand

## Slide 15: 325, 717 Asphalt rubber
Application is in 325
Binder is in 717
Both section now reflect current “state of the art” practices

## Slide 16: MAG 2012
Asphalt Working group

## Slide 17: Asphalt Working Group
2012 major case revisions:
332 protection of uncured surfaces
317 dust control for milling
711 Asphalt Binder spec. added binders, typos
710 added low traffic gyratory spec.
709,710 use of RAP

## Slide 18: Thank you!
This work and all of the cases are done by industry, City engineers, County engineers, MAG engineers.